Finite Element Approximation
Temperature in two dimensions

---
Problem Definition
- On rectilinear domain from (0, 0) to (4, 4)
- Boundary conditions

---
Finite Element Approximation
- Goals
  - Generality
    - Any domain size, any rectangular or triangular grid
      - Any step size in x or y
  - Accuracy
  - Compactness
    - Don’t duplicate work

---
Finite Element Approximation
- Square grid
  - Becomes arbitrary rectangles
- Structured and unstructured rectangular grid
  - Structured grid of arbitrary step sizes
  - Treat structured and unstructured identically

---
Step 1
- Read problem configuration from file
  - Arbitrary minima and maxima
  - Arbitrary step size in x and y
    - x, y step sizes separate
  - Arbitrary k, f, T0
    - k, f, T0 still constant across domain
      - All ai,j still just k
  - Arbitrary boundary conditions
    - Any boundary or boundary portion can be any boundary condition

---
Step 2
- Read element maps and node coordinates from file
  - For structured rectangle and triangle, write maps and coordinates to file for later reading
    - Only need to do this once for each problem configuration
    - x, y step sizes separate
    - Same layout as unstructured triangle data
- Removes need for local to global node mapping calculations
  - All contained in a data structure read from the mapping file

---
Step 3
- Generate element-wise matrices
  - Two functions instead of three
    - Rectangles and triangles
      - Structured vs unstructured is already decided by the mapping file, but be careful not to assume right angles in our triangles
      - Instead, find area, α, β,γ for each triangle based on its node coordinates, then use these to generate
  Removes need for local to global node mapping calculations
  - All contained in a data structure read from the mapping file

---
Step 4
- Build global stiffness matrix and {F}
  - Use element maps to choose the correct rows and columns
    - Each element equation is done in terms of global nodes, so each entry in [Ke]{ue} = {qe} + {fe} is coded by row and column in the global matrix equation

---
Step 5
- Apply Boundary Conditions
  - Check node coordinates data structure to see if a node qualifies for any boundary
  - If so, apply the boundary
    - Dirichlet: remove appropriate row, column from [K], add Ki,j*Tj to Qi
    - Neumann: Qi += condition value

---
Step 6
- Solve:
    - [K]{T} = {Q} for {T}
- Re-insert known nodes into {T}
  - Indexed by global node number

---
Results

---
Results

---
Results

---
Results

---
Results

---
Analysis
- Possible sources of error:
  - Building of individual element equations
    - T(x,y) varies incorrectly in each element
    - T(x,y) outcome depends sensitively on element type
  - Building of global matrix equation
    - T(x,y) not constrained correctly – elements do not mesh
      - Lots of discontinuities
  - Application of BCs
    - T(x,y) flipped, stretched, or skewed
      - Spikes/wells radiating from corners
  - Reintegration of node vector
    - Piecewise discontinuities from BCs tranlation

---
Analysis
- Most likely?
  - Error(s) building individual elements